## Slide 1
Name:
Arash Harirpoosh
Student Number:
9731505
Presentation Title:
RFID Specs

## Slide 2: RFID Components
Consists of two main components:
  Transponder/tag attached to an object to be identified
  Transceiver also know as interrogator/Reader
A Reader in RFID Module:
  Consists of a Radio Frequency Module which generates high frequency electromagnetic field
Tag in RFID Module
  Is a passive device, means that it doesn’t contain a battery
  Contains microchip that stores and processes information, then the antenna receive and transmit a signal

## Slide 3: How Does RFID’s Work?
What happens Inside RFID Module:
  Reader generates electromagnetic field which causes electrons to move through the tag’s antenna and subsequently power the chip
  Powered chip inside the tag then responds by sending its stored information back to the reader in the form of another radio signal. (This is called backscatter)
  Change in the electromagnetic/RF wave or the backscatter, is detected and interpreted by the reader which sends the data out to a computer or microcontroller

## Slide 4: RFID Hardware Overview
Tag
  Have 1 KB memory
  Can store some sort of secrete messages by writing it in a tag
Reader
  Create 13.56 MHz electromagnetic field
  Communicate with a microcontroller over a 4—pin SPI with a maximum data rate of 10Mbps
  Supports communication over I2C and UART protocols
  Operating voltage of the module is from 2.5 to 3.3 V

## Slide 5: RFID Module Pinout
VCC
  Supplies power for the module. This can be anywhere from 2.5 to 3.3 volts
RST
  Input for Reset an power-down
  When goes low, hard power-down is enabled, that turns off all internal current sinks including the oscillator and the input pins are disconnected from the outside world.
  On the rising edge, the module is reset

## Slide 6: RFID Module Pinout
GND
  Ground Pin
IRQ
  interrupt pin that can alert the microcontroller when RFID tag comes into its vicinity
MISO / SCL / Tx
  Acts as Master-In-Slave-Out when SPI interface is enabled
  Acts as serial clock when I2C interface is enabled
  Acts as serial data output when UART interface is enabled

## Slide 7: RFID Module Pinout
MOSI (Master Out Slave In)
  SPI input to the RC522 module
SCK (Serial Clock)
  Accepts clock pulses provided by the SPI bus Master
SS / SDA / Rx
  Acts as Signal input when SPI interface is enabled
  Acts as serial data when I2C interface is enabled
  Acts as serial data input when UART interface is enabled
  It can be used as a reference for identifying the other pins

## Slide 8: References
https://lastminuteengineers.com/how-rfid-works-rc522-arduino-tutorial/#:~:text=RFID%20or%20Radio%20Frequency%20Identification,generates%20high%20frequency%20electromagnetic%20field.