## Slide 1
Name:
Arash Harirpoosh
Student Number:
9731505
Presentation Title:
CoAP Comparison

## Slide 2: CoAP vs MQTT
Architecture
  MQTT
    MQTT is publish/subscribe messaging protocol
    Every message publish to an address, known as topic
    Clients may subscribe to multiple topics
    Runs over TCP
    M:N communication
  CoAP
    Follows client/server model
    Clients make requests to servers, servers send back responses
    Clients may GET, PUT, POST and DELETE resources.
    1:1 comunication

## Slide 3: CoAP vs MQTT
Security
  MQTT
    May require username and password authentication
    To ensure privacy, the TCP connection may be encrypted with SSL/TLS
  CoAP
    Because it is built on top of UDP not TCP, SSL/TLS are not available.
    Instead use DTLS or IPSec

## Slide 4: CoAP vs MQTT
Power Consumption
  MQTT Used more power than CoAP
Packet size
  MQTT has 2 Bytes header
  CoAP has 4 Bytes header
Quality of service
  CoAP
    Confirmable, Non-confirmable, Acknowledgment and Reset messages
  MQTT
    QoS levels in fixed headers(QoS0, QoS1, QoS2)

## Slide 5: References
https://www.eclipse.org/community/eclipse_newsletter/2014/february/article2.php
https://www.pickdata.net/news/mqtt-vs-coap-best-iot-protocol
https://datatracker.ietf.org/meeting/103/materials/slides-103-maprg-evaluating-the-performance-of-coap-mqtt-and-http-in-vehicular-scenarios-jaime-jimenez-00
Lecture-05v2.pdf